## Slide 1: F1490-Z EVK Configuration for 3.3GHz ÷ 3.8GHz, MB Operation
Victor Korol Sept-17, 2019

## Slide 2: F1490-Z EVK Modification for 3.3GHz÷3.8GHz Band
Extra bypass capacitor (Cx) is installed at the above location on the L1-Pin4 trace to define the inductance at the LNA drain. The capacitor location on the trace is important for the S21 peak centering at 3.55GHz. For example, if Cx is shifted up the trace by one width of the 0402 Cx, then the S21 peak will be at 3.8GHz and gain variation across 3.3-3.8GHz will increase to 1dB from 0.5dB variation achieved with the Cx at the pictured location.
0Ω resistor is used instead of L1
Cx = 33pF shunt to GND cap is installed next to the inductor/0Ω res.

## Slide 3: F1490-Z Schematic Modification for 3.3GHz÷3.8GHz Band
Cx is the additional bypass capacitor installed as shunt on the trace connecting pin4/VDD1 and inductor L1.
Cx

## Slide 4: F1490-Z BOM Modification for 3.3GHz÷3.8GHz Band
Cx is the additional bypass capacitor installed on the trace between pin4/VDD1 and inductor L1.
* Updated output match C6, C5 for higher OP1dB
Part Reference | Qty. | Description | Mfr. Part # | Mfr.
C1 | 1 | 0.8pF ±0.1pF, 50V ,COG Surface Mount Capacitor | GJM1555C1HR80BB01D | Murata
C6 (inductor) | 1 | 4.3nH ±0.3nH, 300mA, Surface Mount Inductor | LQG15HS4N3S02 | Murata
C2 | 1 | 6pF ±0.1pF, 50V ,COG Surface Mount Capacitor | GJM1555C1H6R0BB01 | Murata
C3, C7, C10, C9 | 4 | 33pF ±5%, 25V, COG Surface Mount Capacitor | GRM1555C1H330J | Murata
C4, C8 | 2 | 0.1uF ±10%, 16V ,X7R Surface Mount Capacitor (Pad 0603 but use 0402 Capacitor) | GRM155R71C104KA88D | Murata
C11 | 1 | 1uF , 50V | GRM155R60J105K | Murata
C5 | 1 | 1.1pF ±0.1pF, 50V , COG Surface Mount Capacitor | GJM1555C1H1R1BB01 | Murata
R1 | 1 | 1.8kΩ ±5%, 1/10W , 680Ω | ERJ2GEJ182 | Panasonic
R2 | 1 | 150Ω ±5%, 1/16W DNI | ERJ2GEJ151 | Panasonic
R8 - R10 | 3 | 0Ω, 1/10W | ERJ2GE0R00X | Panasonic
L2 | 1 | 1.8nH ±0.3nH, 300mA, Surface Mount Inductor | LQG15HS1N8S02 | Murata
L1 (res 0 Ohm) | 1 | 0Ω, 1/10W | ERJ2GE0R00X | Panasonic
J1 – J5 | 9 | SMA Edge Launch (0.375 inch pitch ground tabs) | 142-0701-851 | Emerson Johnson
J6 | 1 | DNI Headerstrip 1x2 | TBD | 
J7 | 1 | Headerstrip 1x10 | TBD | 
TP1 | 1 | Loop, Black, Phosphor Bronze Wire Loop | 5001 | Keystone electronics
U1 | 1 | F1490Z, GaAs Pre-Driver Amplifier | F1490 | IDT
Cx | 1 | 33pF ±5%, 25V, COG Surface Mount Capacitor | GRM1555C1H330J | Murata

## Slide 5: F1490-Z MB-EVK Low Gain Data, SP
F1490Z Mid Band SP, OIP3, OP1dB. Results are at SMA ports. Apply 0.2dB trace loss to shift the plain to the pins.
Idc 69mA.

## Slide 6: F1490-Z MB-EVK Low Gain Data, OP1dB
F1490Z Mid Band SP, OIP3, OP1dB. Results are at SMA ports. Apply 0.2dB trace loss to shift the plain to the pins.
Idc 69mA.

## Slide 7: F1490-Z MB-EVK Low Gain Data, OIP3
F1490Z Mid Band SP, OIP3, OP1dB. Results are at SMA ports. Apply 0.2dB trace loss to shift the plain to the pins.
Idc 69mA.

## Slide 8: F1490-Z MB-EVK Low Gain Data, NF
NF is de-embedded to the QFN RF pin. Idc 69mA.